## Slide 1
SeFaS -Monitoring avalanches in Northern Norway
using SAR and UAV borne sensors
Eirik Malnes, Markus Eckerstorfer, Rune Storvold, Norut
Regula Frauenfelder, Árni Jónsson, Christian Jaedicke, NGI
Earsel LISSIG, February 2014

## Slide 2: Background
Increasing number of avalanche related accidents in the Tromsø region the last 10 years as a result of increased out-door activity
  Snow mobile accidents
  Back-country skiing
  Road accidents
Since 2000 the number of death accidents in Norway has been around 10 per year. - 50% of these were in the Tromsø-region
SeFaS = Centre for remote sensing of avalanches
Partners: Norut and NGI
Financed regional government in Troms county, Northern Norway and partly by the Norwegian Science Council.
The centre will develop innovative methods for applying sensors in satellites and unmanned aerial vehicles (UAV) for monitoring avalanches.

## Slide 3: SeFaS
Satellite remote sensing
  C-band SAR for detecting melting snow
  High-resolution C-band SAR for detecting avalanche paths
  Studies with X-band SAR, sensitivity to SWE?
UAV borne sensors
  Ortho-photo
  Ground penetrating radar
  Recco/ cell phone detection
Validation
  In situ measurements (stations and sampling
  GPR
Outreach
  Contact with national and regional avalanche authorities

## Slide 4: Wet snow detection
We use C-band SAR (currently Radarsat-2, under the Norwegian RS-2 agreement) to monitor wet snow
Wet snow events during the winter may have both a stabilizing and destabilizing effect, depending on the following development of the snow pack
In 2013 the Tromsø-area experienced an severe winter
  Little snow in the early winter
  Rain on snow event in late February
  March-April a long period with large amounts of snow
  The crust developed in late February, formed an unstable layer upon which many avalanches were released

## Slide 5: Processing chain
Wet snow detection
RS-2
MODIS
MODIS multi-temporal aggregated
RS-2 ref. archive
Snow cover
MODIS
so-sref <-3dB
Wet snow detection using C-band SAR

## Slide 6: Kattfjordeidet 2013

## Slide 7: Meteorology Winter 2013–Tromsø area

## Slide 8: Wet snow detection – value?
C-band SAR can be used to detect snow melt in steep terrain
In the current case we saw that the snow were wet up to ca 600 m altitude.
This altitude coincides with the release zone for many of the avalanches
Wet snow products could be used together with other data types to improve avalanche warning

## Slide 9: Detection of avalanche paths
Previous experiments with high-res optical sensors showed that it is feasible to detect avlanches, but cloud cover is often a problem
Last year we also tested out the use of high-resolution SAR for detection of avalanche paths
We chose to use Radarsat-2 Ultrafine mode
Images were multi-looked and geocoded to 3 m
We were able to detect the avalanches we targeted, and additionally a few others.

## Slide 10: Avalanche path detection
April 9, 2013
April 5, 2013

## Slide 11
Steinfjord, April 5, 2013
Kattfjord, April 9, 2013
UAV cam

## Slide 12: Tromdalen

## Slide 13: Kattfjordeidet

## Slide 14: Signal processing (change vs. summer image)

## Slide 15: UAV
Norut has a fleet of UAV’s developed to carry various payloads under different conditions
Long range
Short range
Also helicopters

## Slide 16
Ny-Ålesund

## Slide 17: UAV Camera
Standard cameras are used to take high-resolution images of avalanches
Images are geocoded using GPS information to ortho-photos
Mapping of avalanche paths has a high value in it self, but also valuable as validation data for other sensors (SAR)
Avalanche, nearby Tromsø, April 2013

## Slide 18: GPR development
We collaborate with the Norwegian Defence research institute
A new C-band sounder in GPR configuration will be tested out this week in Tromsø
As soon as we feel confident, we will also try it out mounted on a UAV-helicopter
A main objective in SeFaS is to test out if this sensor can provide valuable information about depth and layer structure in steep terrain

## Slide 19: Sensor conscept for GPR mounted in unmanned helicopter
GPR

## Slide 20: Snow profiling with GPR Glacier, Svalbard

## Slide 21
Field measurements
Field verification of radar backscatter (snow depth, SWE, wetness)
Field verification of UAV-GPR campaigns (snow depth, snow layering)
Understanding of seasonal snowpack development (skredvarsling, time series)
Validation
Collection of in situ data for validation of results from remote sensing

## Slide 22
Sampling through the winter

## Slide 23
Campaings every 14 days + during airborne campaigns

## Slide 24
Field data is also reported to the national avalanche service varsom.no

## Slide 25: Conclusion
SeFas started January 1, 2014
Many activities are started to test out remote sensing technology that can improve the monitoring of avalanches
We experience great interest in the community and hope that the results will be good!

## Slide 26
UAV’s offers many new
opportunities for avalanche studies

## Slide 27
Thank you !