## Slide 1: Global Land Service- Cryosphere & Water LAKE ICE EXTENT FOR NORTHERN HEMISPHERE
Heinilä K., Mattila O.-P., Metsämäki S., Väkevä S., Luojus K., Schwaizer, G and Nagler T.
EARSeL 3Feb 2020

## Slide 2: Introduction - Lake Ice Extent (LIE)
  LIE product offers near real-time information on the ice conditions
    In-situ stations are located sparsely – EO data are valuable
    Due to the polar darkness obstructing the use of optical data, the LIE product is intended to monitor lake ice conditions from February until the end of lake ice season at high latitudes
Fields of application:
  Numerical weather prediction
  Climate modelling
  Water quality research
  Transportation
  Recreation

## Slide 3: Lake Ice Extent for Northern Europe
Lake Ice Extent: 16.4.2019
  Online in Global Land Service since 03/2017
  250m resolution MODIS based product

## Slide 4: Lake Ice Extent for Northern Hemisphere
1 April 2019
The main advantages of the algorithm developed at SYKE
  Utilization of several spectral bands and indices
  Inclusion of simultaneous cloud detection
  Definition of statistical probability for each pixel
  Simplicity of processing
  Sentinel-3 SLSTR based 500m product
  Easy transition between different satellite sensors
NoData
Ice
Water
Sea area
Cloud
Land

## Slide 5: LIE-NH Watermask
25m resolution water occurrance data were reclassified
  0 – 80 % Land
  80 – 100 % Water
Water bodies were shrinked and resampled from 25m to 500 meters (nearest neighbor)
  Without shrinking the 500m resolution retrieval suffers from mixed pixel effects (land and water), as well as from effects from shallow water

## Slide 6: LIE-NH algorithm
Features of the new algorithm:
  Calculation only on watermask pixels
    Reduces calculation time
    Additionally, areas where lakes will never freeze are excluded
  Use of several bands and band relations
    Increased separation ability
    Reduced effect of varying illumination
  Use of fitted probability distributions
    Determine statistical probability for the estimate
  Use of thermal bands
    Diminate effects of water properties (algae, turbidity)
LIE-NH algorithm is based on Gaussian Mixture Model (GMM) distributions of several reflectance/thermal bands and indices derived from S3-SLSTR data
Number of pixels
Reflectance
0.2
0.4
0.6
0.8
1.0
0
2000
1500
1000
500
For clarity only three components are used in figure. In LIE-NH algorithm the initial number of classes (fitted distributions) is 21 and the number of dimensions is 8: SLSTR channels 1, 2, 5, 6, 8 and 9 and two indices NDSI and NDWI.

## Slide 7: LIE-NH processing

## Slide 8: Validation: In-situ data
In-situ observation ” The whole horizon is ice-free” in Nuasjärvi, Finland, on 26 April 2019
S2 MSI image on 25 April 2019
S2 MSI image on 28 April 2019

## Slide 9: Validation: Sentinel-2 MSI data
Over all 77 images between 7 March and 28 May 2019
  Most lakes are under melting stage, presenting partial ice cover
    23.9% of images includes only ice pixels (including different ice types)
    8.6% of images includes only open water pixels
    67.6.% of images includes lakes with both ice covered and open water pixels
  From Lokka, Finland, and Tjaktjajaure, Sweden, several images during the spring

## Slide 10: Example of validation: Time series from Lake Lokka
Lake Lokka in Finland on 24 May 2019

## Slide 11: Challenges in validation – preparation of S2-based reference data
Lake Hyargas Nuur in Mongolia on 23 April 2019
How to create high resolution lake ice extent maps – ice or open water?
Resampled high resolution data was classified as open water if <50% of the pixels were ice covered
This shows up as “false” ice commissions in the validation results

## Slide 12: Pros and cons
Flathead Lake in USA on 21 April 2019
Recognizes even turbid open water
Very turbid water may be interpreted as cloud
  Temperature limitation aids
North part of Lake Winnipeg on 19 May 2019
Recognizes ice even when it is fragmented
Even small pieces of ice within 500m resolution pixel may increase the reflectance -> the pixel is classified as ice - temperature data does not help

## Slide 13: Pros and cons
Qinghai Lake in China 6 April 2019
Recognizes dark ice well
Glan in Sweden 26 February 2019
When the ice is very dark with water on it, ice is not identified
  Temperature doesn’t help

## Slide 14: Validation results
 | LIE-NH 500m |  | 
S2-LIE | No ice | Ice | N cases
No Ice | 80487 (TN) | 26662 (FP) | 107149
Ice | 6413 (FN) | 75064 (TP) | 79818
N cases | 86900 | 101726 | 188626
Total number of 500 m resolution pixels 188 626
Recall 92.1%
  Percentage of correctly classified ice out of all true ice pixels
False alarm rate 24.9%
  Falsely classified as ice out of all open water pixels
Precision 73.8%
  Percentage of correctly classified ice out of all classified ice pixels
F-Score 82.0%
  The weighted harmonic mean of the precision and recall
Results would seemingly improve if more totally ice-covered and ice-free lakes would be included!
-focus was on complex cases

## Slide 15: Summary - Northern Hemisphere Lake Ice Extent product in 500 m
Review in March 2020
The main advantages of the algorithm
  Utilization of several spectral bands and indices
  Inclusion of simultaneous cloud detection
  Definition of statistical probability for each pixel
  Simplicity of processing
Validation results
  Recall 92.1% (Percentage of correctly classified ice out of all true ice pixels)
    Detect different kind of ice covers well
    Water on ice: method cannot always detect if the water is on ice or is it open water
  False alarm rate 24.9% (Falsely classified as ice out of all open water pixels)
    Detect open water well (validation dataset includes mostly complicated cases where both ice and water is presented)
    Fracmented ice cover causes challenges
      In our case resampled high resolution data was classified as open water if <50% of the pixels were ice covered

## Slide 16
Thank you!