## Slide 1: Validation of ESA CCI+ Snow Products
Carlo Marin, Claudia Notarnicola, Sari Metsämäki, Valentina Premier, Kathrin Nägeli, Arnt-Børre Salberg, Gabriele Schwaizer, Rune Solberg, Andreas Wiesmann, Stefan Wunderle, Thomas Nagler, Anna Marie Trofaier
9th EARSeL Workshop, Bern

## Slide 2: Validation objectives
The objectives of the validation activities are:
  Quantify the error of the snow_cci products;
  Characterize the performance against:
    Seasonality;
    Forest presence;
    Local topography.
  Quantify the error of the provided snow_cci uncertainty.
Independent from algorithm development.

## Slide 3: Validation Workflow
Collect representative HR images
Generate HR SCE
Preparation of the data
SCF high resolution intercomparision
In-situ validation of SCF and SWE
Other SCF/SWE products intercomparison
Uncertainty validation
Documentation of the results
Collect representative in-situ measurements
Format the in-situ data in the ESA snow CCI format
Collect representative SCF/SWE maps
Preparation of the data
Landsat/Sentinel-2
In-situ measurements
Other SCF/SWE products
Ancillary data
DEM
Water masks
Land cover
Climate zones
snow_cci reference dataset
snow_cci validation activities
Data Preparation
snow_cci SWE products
snow_cci SCF products
snow_cci SWE products validation
snow_cci SCF products validation

## Slide 4: SCF Validation Protocol

## Slide 5: SCF Validation: in-situ validation
All products and in-situ data are treated as binary (snow/no-snow) using the following snow depth binary conversion thresholds:
  SD=0cm;
  SD=2cm;
  SD=15cm.
SCF binary conversion thresholds:
  SCF=25%;
  SCF=50%.
Inhomogeneous neighborhood is rejected from validation.
Results are divided according to:
  different land-cover classes (forest, non-forest, mountain, plain)
  four three-month periods: October-December, January-March, April- June, July-September
Metrics: True/False positive, recall, precision, false alarm rate, accuracy, critical success index, f-score.
Workflow for the in-situ comparison.
Snow_cci SCF products
Pre-processing

## Slide 6: SCF Validation: in-situ validation
In-situ data snow depth observations

## Slide 7: SCF Validation: HR validation
HR snow cover maps derived according to State-of-the-art snow algorithms:
  Dozier and Painter (2004): binary snow on ground;
  Klein et al. (1998): binary snow on ground;
  Salomonson and Appel (2006): viewable fractional snow cover.
The HR intercomparison is carried out at the lowest resolution between the snow_cci SE maps and the intercompared maps.
The following steps are required for the intercomparison:
  Pixel aggregation;
  Identification of valid pixels;
  Masking considering the ancillary data;
  Intercomparison.
Pixel-by-pixel intercomparison metrics: bias, RMSE, unbiased RMSE, CorrCoef, True/False positive, True/False negative.
Analysis of different land surface classes (forest, non-forest, mountain, plain) in the intercomparison process.
Workflow for the HR inter-comparison.
Snow_cci SCF products

## Slide 8: SCF Validation: HR intercomparison
Landsat images selected for the validation
~800 scenes spanning 1986-2018

## Slide 9: SCF Validation: Intercomparison
Workflow for the SE inter-comparison.
Inter-comparison between different SCF and snow binary products (CP1).
All the comparisons are done at the lowest resolution.
Pixel-by-pixel intercomparison metrics: bias, RMSE, unbiased RMSE, CorrCoef, True/False positive, True/False negative
Analysis of different land surface classes (forest, non-forest, mountain, plain) in the intercomparison process.

## Slide 10: SWE Validation Protocol

## Slide 11: SWE Validation: in-situ validation

## Slide 12: SWE Validation: intercomparison
Product Name | Meteorology | Time Period | Data Source
Crocus v8 | ERA-Interim | 1979-2018 | ECCC
Brown | ERA-Interim | 1979-2018 | ECCC
MERRA2 | MERRA2 | 1980-- | GMAO, 2015
ERA5 | ERA5 | 1979-- | C3S, 2017
GLDAS-2.1 | GDAS/GPCP | 2010-- | Beaudoing, 2016
Agreement between the snow_cci products and LSM products is assessed using metrics of bias, RMSE and correlation.
Notes: The results are not yet available.

## Slide 13: SCF Validation Results

## Slide 14: SCF Validation Results: in-situ
Statistics obtained by considering 419 MODIS available and 2M of in-situ measurements for the different combination of thresholds.
binary metrics.
contingency matrix
SD threshold [m] | 0 | 0 | 0.02 | 0.02 | 0.15 | 0.15
SCF threshold [%] | 25 | 50 | 25 | 50 | 25 | 50
Recall | 0.85 | 0.76 | 0.87 | 0.80 | 0.94 | 0.90
Precision | 0.94 | 0.96 | 0.90 | 0.93 | 0.62 | 0.67
False Alarm Rate | 0.00 | 0.00 | 0.01 | 0.00 | 0.03 | 0.02
Hit Rate (Accuracy) | 0.98 | 0.98 | 0.98 | 0.98 | 0.97 | 0.98
Critical Success Index | 0.80 | 0.74 | 0.80 | 0.75 | 0.60 | 0.62
F-score | 0.89 | 0.85 | 0.89 | 0.86 | 0.75 | 0.76
TSD | 0 |  | 0 |  | 0.02 |  | 0.02 |  | 0.15 |  | 0.15 | 
TSCF | 25 |  | 50 |  | 25 |  | 50 |  | 25 |  | 50 | 
 | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow
Snow | 84.60 | 15.40 | 76.50 | 23.50 | 87.50 | 12.50 | 79.96 | 20.04 | 94.17 | 5.83 | 89.78 | 10.22
No-Snow | 0.46 | 99.54 | 0.28 | 99.72 | 0.74 | 99.26 | 0.46 | 99.54 | 2.75 | 97.25 | 2.07 | 97.93
Notes: The best accuracy is 98%. As expected by increasing the threshold on SCF from 25% to 50% we are losing in sensitivity i.e., the recall decreases. Whereas, by increasing the threshold on the SD the recall increases at the expenses of the other metrics. This means that the snow_cci products are able to identify shallow snowpack or patchy situations well.

## Slide 15: SCF Validation Results: in-situ
Statistics obtained by considering 810 AVHRR available and 3.8M of in-situ measurements for the different combination of thresholds.
binary metrics.
contingency matrix
SD threshold [m] | 0 | 0 | 0.02 | 0.02 | 0.15 | 0.15
SCF threshold [%] | 25 | 50 | 25 | 50 | 25 | 50
Recall | 0.89 | 0.84 | 0.90 | 0.85 | 0.93 | 0.91
Precision | 0.89 | 0.92 | 0.85 | 0.88 | 0.49 | 0.52
False Alarm Rate | 0.01 | 0.01 | 0.02 | 0.01 | 0.05 | 0.04
Hit Rate (Accuracy) | 0.98 | 0.98 | 0.98 | 0.98 | 0.95 | 0.96
Critical Success Index | 0.80 | 0.78 | 0.77 | 0.76 | 0.47 | 0.49
F-score | 0.89 | 0.88 | 0.87 | 0.87 | 0.64 | 0.66
TSD | 0 |  | 0 |  | 0.02 |  | 0.02 |  | 0.15 |  | 0.15 | 
TSCF | 25 |  | 50 |  | 25 |  | 50 |  | 25 |  | 50 | 
 | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow | Snow | No-Snow
Snow | 88.63 | 11.37 | 83.96 | 16.04 | 89.65 | 10.35 | 85.36 | 14.64 | 93.16 | 6.84 | 90.62 | 9.38
No-Snow | 1.18 | 98.82 | 0.74 | 99.26 | 1.63 | 98.37 | 1.08 | 98.92 | 5.19 | 94.81 | 4.17 | 95.83
Notes: The best accuracy is 98%. As expected by increasing the threshold on SCF from 25% to 50% we are losing in sensitivity i.e., the recall decreases. Whereas, by increasing the threshold on the SD the recall increases at the expenses of the other metrics. This means that the snow_cci products are able to identify shallow snowpack or patchy situations well.

## Slide 16: SCF Validation Results: in-situ
Statistics obtained by considering 419 MODIS available and 2M of in-situ measurements for the different combination of thresholds in forest and unforested areas.
SD threshold [m] | 0 | 0 | 0.02 | 0.02 | 0.15 | 0.15
SCF threshold [%] | 25 | 50 | 25 | 50 | 25 | 50
Recall | 0.82 | 0.71 | 0.83 | 0.73 | 0.90 | 0.83
Precision | 0.94 | 0.96 | 0.92 | 0.94 | 0.73 | 0.78
False Alarm Rate | 0.01 | 0.00 | 0.01 | 0.01 | 0.03 | 0.02
Hit Rate (Accuracy) | 0.97 | 0.97 | 0.97 | 0.97 | 0.97 | 0.97
Critical Success Index | 0.78 | 0.69 | 0.77 | 0.69 | 0.67 | 0.67
F-score | 0.87 | 0.81 | 0.87 | 0.82 | 0.81 | 0.80
forest
SD threshold [m] | 0 | 0 | 0.02 | 0.02 | 0.15 | 0.15
SCF threshold [%] | 25 | 50 | 25 | 50 | 25 | 50
Recall | 0.86 | 0.79 | 0.89 | 0.83 | 0.96 | 0.93
Precision | 0.94 | 0.95 | 0.89 | 0.92 | 0.57 | 0.61
False Alarm Rate | 0.00 | 0.00 | 0.01 | 0.00 | 0.03 | 0.02
Hit Rate (Accuracy) | 0.99 | 0.98 | 0.99 | 0.99 | 0.97 | 0.98
Critical Success Index | 0.81 | 0.76 | 0.81 | 0.77 | 0.55 | 0.59
F-score | 0.89 | 0.86 | 0.89 | 0.87 | 0.71 | 0.74
Open field
Notes: the accuracy in forested areas decrease of about 2% in terms of hit rate and F-score for both the sensors. This is an expected result given the well-known issues of identifying snow in forested areas using optical remote sensing data.

## Slide 17: SCF Validation Results: in-situ
Statistics obtained by considering 810 AVHRR available and 3.8M of in-situ measurements for the different combination of thresholds in forest and unforested areas.
forest
Open field
SD threshold [m] | 0 | 0 | 0.02 | 0.02 | 0.15 | 0.15
SCF threshold [%] | 25 | 50 | 25 | 50 | 25 | 50
Recall | 0.74 | 0.68 | 0.75 | 0.69 | 0.83 | 0.79
Precision | 0.94 | 0.95 | 0.93 | 0.94 | 0.76 | 0.78
False Alarm Rate | 0.01 | 0.00 | 0.01 | 0.01 | 0.02 | 0.02
Hit Rate (Accuracy) | 0.96 | 0.96 | 0.96 | 0.96 | 0.96 | 0.97
Critical Success Index | 0.71 | 0.65 | 0.71 | 0.66 | 0.66 | 0.65
F-score | 0.83 | 0.79 | 0.83 | 0.79 | 0.80 | 0.79
SD threshold [m] | 0 | 0 | 0.02 | 0.02 | 0.15 | 0.15
SCF threshold [%] | 25 | 50 | 25 | 50 | 25 | 50
Recall | 0.91 | 0.87 | 0.92 | 0.88 | 0.96 | 0.94
Precision | 0.88 | 0.91 | 0.84 | 0.87 | 0.46 | 0.48
False Alarm Rate | 0.01 | 0.01 | 0.02 | 0.01 | 0.06 | 0.04
Hit Rate (Accuracy) | 0.98 | 0.98 | 0.98 | 0.98 | 0.95 | 0.95
Critical Success Index | 0.81 | 0.80 | 0.78 | 0.78 | 0.45 | 0.47
F-score | 0.90 | 0.89 | 0.88 | 0.88 | 0.62 | 0.64

## Slide 18: SCF Validation Results: HR validation
 | Salomonson | Klein | Dozier
RMSE | 13.995 | 19.415 | 15.474
Unbiased RMSE | 13.629 | 18.265 | 15.038
Bias | -3.180 | -6.585 | -3.648
Correlation Coefficient | 0.952 | 0.917 | 0.943
 | Salomonson | Klein | Dozier
RMSE | 20.536 | 21.634 | 21.307
Unbiased RMSE | 20.535 | 21.253 | 21.257
Bias | 0.247 | -4.042 | -1.450
Correlation Coefficient | 0.890 | 0.883 | 0.884
Overall results of the validation of the snow_cci products:
MODIS-derived
AVHRR-derived
User requirements:
Unbiased RMSE < 20%

## Slide 19: SCF Validation Results: HR validation
Overall results of the validation of the snow_cci products in forested and unforested areas:
MODIS-derived
AVHRR-derived
User requirements:
Unbiased RMSE < 20%
 | Salomonson forested | Salomonson open areas
RMSE | 24.801 | 19.473
Unbiased RMSE | 24.790 | 19.468
Bias | -0.730 | 0.462
Correlation Coefficient | 0.799 | 0.905
 | Salomonson forested | Salomonson open areas
RMSE | 18.882 | 12.495
Unbiased RMSE | 17.228 | 12.325
Bias | -7.728 | -2.055
Correlation Coefficient | 0.909 | 0.962

## Slide 20: SWE Validation Results

## Slide 21: SWE Validation Results: in-situ
Finnish snow course results
Bias: -5 mm
RMSE: 40 mm
Notes: While RMSE is higher under deep snow conditions (SWE>200 mm), these only represent approximately 4% of the validation dataset. The slight fluctuations are generally due to the characteristics of the seasonal snowpack (i.e., wet or dry seasons). Nonetheless, for the time span considered the performance of the algorithm is stable.

## Slide 22: SWE Validation Results: in-situ
Russian snow course results
Bias: -9 mm
RMSE: 52 mm
Notes: While RMSE is higher under deep snow conditions (SWE>200 mm), these only represent approximately 4% of the validation dataset. The slight fluctuations are generally due to the characteristics of the seasonal snowpack (i.e., wet or dry seasons). Nonetheless, for the time span considered the performance of the algorithm is stable.

## Slide 23: SWE Validation Results: in-situ
Canadian snow course results
Bias: -28 mm
RMSE: 71 mm
Notes: While RMSE is higher under deep snow conditions (SWE>200 mm), these only represent approximately 4% of the validation dataset. The slight fluctuations are generally due to the characteristics of the seasonal snowpack (i.e., wet or dry seasons). Differently from the previous assessments, at the beginning of the time series the performance is slightly worse than after the late eighties. This can be due to characteristics of the Scanning Multichannel Microwave Radiometer (SMMR) which operated between 1978 and 1987

## Slide 24: Conclusions
A validation protocol based on the well-established protocol developed in the Satellite Snow Product Intercomparison and Evaluation Exercise (SnowPEx) has been defined for snow_cci.
SNOW COVER FRACTION:
Reference data set consisting of >3.8 million and >2 million in-situ measurements & 833 and 410 high resolution SCE maps for AVHRR and MODIS used for validation activities in the first year.
Product performance was assessed considering also different surface and topography conditions
High accuracy for SCF products from both the sensors from validation with in-situ data:
  Hit Rate > 95% for all the thresholds combinations
  F-score > 87% for SCF ≥ 25% and SD ≥ 0 m and SD ≥ 0.02 m
For validation with high resolution snow maps:
  Overall unbiased RMSE < 19% and < 21% for MODIS and AVHRR  compliant with the user requirements.
  Overall bias < 4% and < 6% for AVHRR and MODIS, respectively
  Correlation coefficient > 0.91 for MODIS and > 0.88 for AVHRR.

## Slide 25: Conclusions and future work
SNOW WATER EQUIVALENT
In order to assess the quality of the snow_cci SWE product v1.0, we compared it with an extensive and a diverse ground-based reference dataset from Russia, Finland and Canada, spanning the years 1979-2018.
The overall retrieval accuracy for the SWE product, for all investigated samples was around 50 – 70 mm. The overall bias was around 10 – 20mm. The range of these values depend on the reference data and the region.
For most snowpacks (all but the 5% of the deepest snowpacks), the SWE retrieval fulfils the user requirements with an RMS error of 42.5 mm.
Validation results reflect a good overall performance of the snow_cci SCF products
Accuracies of snow_cci products generated in the first year fulfil the user requirements
Reference data set will be extended in the second year, and each future product version will be evaluated and quality checked.

## Slide 26: SCF Validation Results: HR validation
Overall results of the validation of the snow_cci products in mountains and plains:
MODIS-derived
AVHRR-derived
User requirements:
Unbiased RMSE < 20%
 | Salomonson | Klein | Dozier
RMSE | 13.259 | 16.393 | 14.136
Unbiased RMSE | 13.015 | 15.841 | 13.937
Bias | -2.533 | -4.216 | -2.361
Correlation Coefficient | 0.958 | 0.940 | 0.953
 | Salomonson | Klein | Dozier
RMSE | 14.391 | 20.921 | 16.177
Unbiased RMSE | 13.948 | 19.366 | 15.575
Bias | -3.542 | -7.915 | -4.371
Correlation Coefficient | 0.945 | 0.895 | 0.933
 | Salomonson | Klein | Dozier
RMSE | 20.961 | 22.182 | 21.086
Unbiased RMSE | 20.799 | 21.591 | 20.809
Bias | -2.602 | -5.087 | -3.405
Correlation Coefficient | 0.899 | 0.894 | 0.901
 | Salomonson | Klein | Dozier
RMSE | 20.361 | 21.408 | 21.396
Unbiased RMSE | 20.313 | 21.100 | 21.386
Bias | 1.402 | -3.618 | -0.656
Correlation Coefficient | 0.861 | 0.851 | 0.848
mountains
mountains
plains
plains

## Slide 27: SCF Validation Results: HR validation
MODIS-derived
Dozier
Klein
Salomonson
User requirements:
Unbiased RMSE < 20%

## Slide 28: SCF Validation Results: HR validation
Dozier
AVHRR-derived
Klein
Salomonson
User requirements:
Unbiased RMSE < 20%