## Slide 1
ODTU
Quantifying Snow Water Equivalent by
Integration of UAS and GPR Surveys
PhD Student Semih YILDIZ1, METU, TURKEY
Prof. Dr. Zuhal AKYUREK2 , METU, TURKEY
Prof. Dr. Andrew BINLEY3 , Lancaster Univ., UK
03 - 05 February 2020, Bern, Switzerland

## Slide 2
HSn
HN
SWE
HSn+1
2/51
-
Snow depth (HS)
24 h new snow depth (HN)
Snow Review: What are the snow parameters?
Snow Water Equivalent (SWE)
https://www.slideshare.net/pelacia/mysnowmaps-snow-maps-display-and-snow-data-crowdsourcing

## Slide 3
Snow Review: How are the snow parameters measured?

## Slide 4
Snow Review: UAS-Photogrammetry in Snow Survey
UAS-Photogrammetry are emerging as a potential low-cost technique to yield spatially continuous snow depth measurements (Avanzi et al. 2018; Bühler et al., 2016).
UAS are flexible platforms in terms of acquisition time and region of interest (Whitehead et al., 2014)
UAS is used to acquire images of the study area with optical cameras having cm scale ground resolution (Avanzi et al. 2018).
The output is a very high-resolution digital surface model (DSM) of the survey area.
Spatially continuous snow depths of the study area are obtained by simply subtracting a non-snow DSM from a snow covered DSM.
But.................
What about snow density snd SWE?

## Slide 5
Snow Review: GPR in Snow Survey
GPR surveys can be effectively used to determine snow properties (Holbrook, Miller, & Provart, 2016).
GPR surveys provide two-way travel times of radar reflections (e.g. at the base of snow pack), typically along a transect.
Converting travel times to depth requires measurement or estimates of the radar velocity.
GPR has been shown to be an effective tool for measuring snow density because of the close relationship between dry snow density and radar velocity. (St. Clair and Holbrook, 2017).
But......
Velocity estimations from radar reflections are limited to number of reflective objects.

## Slide 6
A New Approach: UAS-Photogrammetry and GPR Cooperation

## Slide 7
7/51
-
The study area (7 ha) is the Ilgaz Mountains National Park catchment located in the northwest of Turkey
The catchment has a surface area of approximately 45 km2, with a mean elevation of about 1800 m. The annual mean air temperature is 5.7 °C.
Study Area

## Slide 8
8/51
-
GPR
UAS
GNNS
Snow Sampler Tube
Snow Mobile
Equipments

## Slide 9
9/51
-
Forward overlap : 75%
Side overlap: 75%
Area:7.4 ha
Flight height:80 m.
GSD:2.5 cm
Flight speed: 12 m/s
Image acquisition time: 14:08-14:17
120 images were acquired.
Flight Plan (Summer)
Flight Plan (Winter)
Flight speed: 6 m/s
Image acquisition time: 09:42-09:48
118 images were acquired.
Forward overlap : 80%
Side overlap: 60%
Area:26.4 ha
Flight height:150 m.
GSD: 5.9 cm
Fieldwork:UAS Surveys

## Slide 10
10/51
-
UAS based Snow Depth
(a) HS from DSM-DSM Differences (6 cm/pixel)
(b) HS from DSM-DTM
Differences(6 cm/pixel)

## Slide 11
11/51
-
GPR data processing steps
(Reflexw Software):
resetting the traces to the time zero
DC shift Removal
Dewow
time gain function
background removal
median filter to remove antenna ringing.
Pick snow depths
Pick velocity from Hyperbolic Reflection
GPR based Snow Depth

## Slide 12
12/51
-
c is speed of light in vacuum (~0.3 m/ns)
r is snow density (kg/m3)
is radar velocity in snow layer
is real part of the dielectric constant
 | Relative Permittivity | EM Velocity (m / ns)
snow | 1.4 - 3.2 | 0.168 - 0.254
Sea Ice | 4 - 8 | 0.106 - 0.150
Dry Soil | 3 - 8 | 0.110 - 0.170
GPR based Snow Depth
Bradford, J., Harper, J., & Brown, J. (2009). Water Resources Research, 45, W08403. https://doi.org/10.1029/2008WR007341
r max=362 kg/m3 v max=0.230 m/ns

## Slide 13
13/51
-
The two-way travel time (TWT) of GPR signals and snow depths obtained for Line-
1 and Line-2. Velocity was obtained from buried plate reflection.
GPR based Snow Depth

## Slide 14
14/51
-
Illustrations of snow depths obtained from GPR, UAS and Snow Tube observations and the canopy heights (HC) along Line 2.
Effects on Canopy on UAS based HS

## Slide 15
15/51
-
Histogram of snow densities determined from snowmobile GPR measurements (total of 670 points). The mean density is 0.353 g/cm3.
UAS and GPR based Snow Densities

## Slide 16
16/51
-
SWEs measured via Snow Tube vs SWEs estimated from DSM-DSM differences multiplied by IDW based snow density derived from GPR TWT and UAV HS.
(a) SWEs of points located on canopy-free areas
(b) SWEs of points located on canopy covered areas
Effects of Canopies on UAS - GPR based SWE

## Slide 17
17/51
-
SWE from DSM-DSM Differences multiplied by GPR derived density
SWE from DSM-DTM Differences multiplied by GPR derived density
SWE from DSM-DSM Differences multiplied by IDW based density derived from GPR TWT and UAS HS
SWE from DSM-DTM Differences multiplied by IDW based density derived from GPR TWT and UAS HS
UAS-GPR based SWE

## Slide 18
18/51
-
Table 1. Snow depths accuracies were evaluated based on manual snow measurements. Tube refers to the manual measurement.
Results:

## Slide 19
19/51
-
Table 2. Snow density estimation accuracies were assessed in reference to manual snow tube measurements.
Results:

## Slide 20
20/51
-
SWE (mm) | Snow Tube | GPRMOBILE HSSURFACE HSTERRAIN |  | GPRPLATE HSSURFACE HSTERRAIN | 
 | Mean | Mean RMSE | Mean RMSE | Mean RMSE | Mean RMSE
Canopy-Free (17 Points) | 370 | 389 ±39 | 407 ±63 | 384 ±33 | 407 ±58
Canopy-Covered (10 Points) | 352 | 241 ±146 | 352 ±86 | 246 ±143 | 356 ±75
Total Samples (27Points) | 363 | 334 ±94 | 387 ±72 | 333 ±91 | 388 ±65
Table 3. Snow water equivalent (SWE) accuracies were evaluated based on manual snow measurements
Results:

## Slide 21
21/51
-
Snow depths and Snow Water Equivalents can be obtained in less time with a UAS-GPR cooperation than manual methods, although significant data processing is needed.
Spatially continuous model of SWEs provides opportunity to observe the effects of environmental parameters such as canopy cover, slope, and topography.
Although we have focused efforts on a relatively small study area, the approach can be adopted at a much larger spatial scale, thus offering immense value for basin-scale hydrology.
Conclusions